## Slide 1: Deep Learning Models for Coronary Artery Disease Classification using Phonocardiograms
Chenhe Liu The British School of Beijing. Beijing, China | Jiasheng Zhang Anhui International Studies University Wuhu, China Nanomega Research Institute Beijing, China | Yibo Zhang Nanomega Research Institute Beijing, China Gezhi Future Research Institute Beijing, China School of Systems and Computing, UNSW Australia

## Slide 2: Introduction
Problem Context:
Cardiovascular diseases, especially coronary artery disease (CAD), are a major global health issue.
Early diagnosis using non-invasive techniques (phonocardiograms, PCGs) can dramatically improve outcomes.
Objective:
Use deep learning to classify heart sounds into normal and abnormal categories.
Compare three different deep learning models: Custom CNN, Transfer Learning (VGG16/MobileNetV2), and PSO-optimized CNN.
Motivation:
Overcome subjectivity in traditional auscultation.
Leverage advanced feature extraction from spectrograms derived via STFT (Short-Time Fourier Transform).

## Slide 3: Literature Review
Deep Learning for PCG Classification:
Previous work (Xiao et al., Ren et al.) has explored CNN architectures with raw waveforms and scalogram images.
Use of pretrained models with transfer learning (e.g., VGG16) has demonstrated improvements.
Feature Extraction Techniques:
Traditional methods: MFCC, LPC, and wavelet transforms.
Recent advancements include STFT-based spectrogram extraction, offering rich time-frequency information.
Optimization Methods:
Introduction of evolutionary algorithms like Particle Swarm Optimization (PSO) to optimize CNN parameters.
Gap Addressed:
The research compares different models to provide a comprehensive evaluation in terms of precision, recall, and F1-score for CAD classification.

## Slide 4: Methodology
Data Preparation:
Dataset: Derived from the 2016 PhysioNet/CinC Challenge; includes over 3,000 PCG recordings.
Pre-processing:
  Resampling to 2,000 Hz.
  Application of a third-order Butterworth band-pass filter with cutoffs at 25 Hz and 200 Hz.
Feature Extraction – Spectrograms:
Short-Time Fourier Transform (STFT):
  Formula (1): X[m,ω]=∑n​x[n]w[n−m]e−jωn
  Formula (2): S[m,ω]=∣X[m,ω]∣
  Formula (3): ϕ[m,ω]=arg(X[m,ω])

## Slide 5
Model Architectures:
Custom CNN:
  Multiple convolutional layers with ReLU activation.
  Use of max pooling and dropout before fully connected layers.
  Key Formulas:
    Convolution: Y=(W⋅X+b
    ReLU Activation: Y=max(0,X)
    Sigmoid (Output Layer): Y=1+e−X1​​
Transfer Learning:
  Models: VGG16 and MobileNetV2.
  Replace final fully connected layers; freeze pretrained weights.
  Use of global average pooling.
PSO-Optimized CNN:
  Optimization using Particle Swarm Optimization.
  PSO Equations:
    Velocity Update: V(t+1)=w⋅V(t)+c1​⋅rand()⋅(Pbest​−X(t))+c2​⋅rand()⋅(Gbest​−X(t))
    Position Update: X(t+1)=X(t)+V(t+1)

## Slide 6: Results and Discussion
Evaluation Metrics:
Accuracy, Precision, Recall, F1-score.
Formulas:
  Accuracy: Accuracy=TP+TNTP+TN+FP+FN\text{Accuracy} = \frac{TP + TN}{TP + TN + FP + FN}Accuracy=TP+TN+FP+FNTP+TN​
  Precision: Precision=TPTP+FP\text{Precision} = \frac{TP}{TP + FP}Precision=TP+FPTP​
  Recall: Recall=TPTP+FN\text{Recall} = \frac{TP}{TP + FN}Recall=TP+FNTP​
  F1-Score: F1=2×Precision×RecallPrecision+RecallF1 = \frac{2 \times \text{Precision} \times \text{Recall}}{\text{Precision} + \text{Recall}}F1=Precision+Recall2×Precision×Recall​

## Slide 7
Model Performance Comparison:
Custom CNN:
  Average F1-score ≈ 0.82.
  Trade-offs observed: high recall for abnormal sounds and lower precision for normal sounds.
Transfer Learning:
  VGG16: F1-score ≈ 0.96.
  MobileNetV2: F1-score ≈ 0.98 (best overall performance).
PSO-Optimized CNN:
  Highest precision for normal sounds but overall lower F1-score (≈ 0.71) due to imbalanced recall.
Discussion Points:
The superior performance of transfer learning architectures underscores the benefit of leveraging pretrained weights.
PSO-enhanced optimization shows promise but may require further tuning to balance precision and recall.

## Slide 8: Conclusion
Key Takeaways:
Deep learning models significantly improve the automatic classification of PCGs for CAD diagnosis.
Transfer Learning (especially MobileNetV2) achieves the best balance and highest F1-score.
Feature extraction using STFT-based spectrograms is effective in capturing critical time-frequency information.
Future Directions:
Exploration of Vision Transformers and Convolutional Autoencoders for further performance enhancement.
Refinement of optimization strategies like PSO to better balance evaluation metrics.
Final Thoughts:
The work demonstrates how rigorous mathematical analysis and advanced neural network architectures converge to solve complex medical diagnostic challenges.
This research bridges the gap between engineering innovations and clinical requirements, ultimately paving the way for better patient outcomes.